SPF5189Z Design Notes
Daniel H. Tatum
Revision 0
08/02/20

# Introduction
The Qorvo SPF5189Z meets frequency and gain requirements while delivering excellent linearity with an OIP3 of 39.5dBm. The output power of +22.5dBm at the 1dB compression point makes the amplifier an ideal driver for a 4W-8W power amplifier.Integration requires a +5V power supply at 90mA of current, band-limiting matching networks, and DC blocking capacitors at both the input and output terminals. The SOT-89-3 package is simple to install in a home lab with a board heater and quality soldering iron.
# Matching Network Design
Discrete matching networks are designed in the Quite Universal Circuit Simulator using manufacturer provided scattering parameter data and built-in microstrip models.
## Stability Circles
A check of the Rollett stability factor indicates that a stable match on both the input (red) and output (blue) networks can be made anywhere on the Smith Chart as in Figure 1.

Figure 1. Qucs Simulation deck for Rollett stability factor.
## Input Network
The input network is a 2nd order Chebyshev bandpass matching network which converts from the system characteristic impedance to the lower gate input impedance.

## Output Network
The output network is a 3rd order Chebyshev bandpass matching network with converts from the drain output impedance to the lower system characteristic impedance.